## Slide 1: AOI defect cogiscan data analysis
07/01/2025

## Slide 2: Current challenges with the AOI data
The data is not clean since it contains
  All the machine calls with False calls
  The overridden calls
  Multiple lines for each CRD failures
Example:
  BSE2503320319 has total 526 lines of defect data
    This board ran 3 times in Bottom AOI, 1 time in top AOI and 1 time in SPI
  The true total true defects were total 6 RDs

## Slide 3: Event time stamp for BSE2503320319
Timestamp | Machine Timestamp | Operation | Machine | Disposition | Is Review | Disposition True failures | Loop number | Machine call/ Inspector call
5/19/2025 1:05 | 5/19/2025 1:05 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE | R1556, R1557 | 1 | Machine
5/19/2025 1:08 | 5/19/2025 1:08 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE |  | 2 | Operator
5/19/2025 11:30 | 5/19/2025 11:30 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE | U1516 | 3 | Machine
5/19/2025 11:43 | 5/19/2025 11:43 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE |  | 4 | Operator
5/19/2025 11:44 | 5/19/2025 11:44 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE |  | 5 | Operator
5/21/2025 5:08 | 5/21/2025 5:08 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE | Q36,Q57,U1500 | 6 | Machine
5/21/2025 5:11 | 5/21/2025 5:11 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE |  | 7 | Operator
6/14/2025 8:19 | 6/14/2025 8:19 | AOI (BOT) | AUS-AOI-L1A-BOT | Reworkable | FALSE | Board pass | 8 | Machine
6/14/2025 8:23 | 6/14/2025 8:23 | AOI (BOT) | AUS-AOI-L1A-BOT | False Call | FALSE |  | 9 | Operator
6/18/2025 11:27 | 6/18/2025 11:27 | SPI (TOP) | AUS-SPI-L1A-TOP | Reworkable | FALSE | Pass | 2 | Machine
6/18/2025 11:28 | 6/18/2025 11:28 | SPI (TOP) | AUS-SPI-L1A-TOP | False Call | TRUE |  | 3 | Operator
6/18/2025 11:43 | 6/18/2025 11:43 | AOI (TOP) | AUS-AOI-L1A-TOP | Reworkable | FALSE | Pass | 1 | Machine
6/18/2025 11:54 | 6/18/2025 11:54 | AOI (TOP) | AUS-AOI-L1A-TOP | False Call | FALSE |  | 2 | Operator

## Slide 4: Event time stamp for BSE2503320319
EventDate | 05/19 (1st time) |  | 
Count of ReworkStatus | Column Labels |  | 
Row Labels | False call | Overridden | Reworkable
AUS-AOI-L1A-BOT |  |  | 
R1556 |  | 1 | 2
R1557 |  | 1 | 2
U1516 | 1 | 1 | 1
U1516.5 | 2 | 2 | 2
U1516.6 | 2 | 2 | 2
U1516.7 | 2 | 2 | 2
U1516.8 | 2 | 2 | 2
Grand Total | 9 | 11 | 13
EventDate | 05/19 (2nd time) |  | 
Count of ReworkStatus | Column Labels |  | 
Row Labels | False call | Overridden | Reworkable
AUS-AOI-L1A-BOT |  |  | 
R1556 |  | 1 | 
R1557 |  | 1 | 
R1557.2 | 1 | 1 | 1
U1516 |  | 2 | 1
U1516.5 | 2 | 6 | 4
U1516.6 | 1 | 6 | 5
U1516.7 | 1 | 5 | 3
U1516.8 | 2 | 6 | 4
Grand Total | 7 | 28 | 18
EventDate | 05/21 ( 3rd time) |  | 
Count of ReworkStatus | Column Labels |  | 
Row Labels | False call | Overridden | Reworkable
AUS-AOI-L1A-BOT |  |  | 
D2609 | 2 | 2 | 2
D5850 | 2 | 2 | 2
Q22 | 1 | 1 | 1
Q36 |  | 3 | 6
Q57.1 |  | 1 | 2
R1557.2 |  | 1 | 
U1500 | 1 | 2 | 3
U1516.5 |  | 2 | 
U1516.6 |  | 2 | 
U1516.7 |  | 1 | 
U1516.8 |  | 2 | 
Grand Total | 6 | 19 | 16

## Slide 5: Event time stamp for BSE2503320319
EventDate | 06/14 ( 4th time) |  | 
Count of ReworkStatus | Column Labels |  | 
Row Labels | False call | Overridden | Reworkable
AUS-AOI-L1A-BOT |  |  | 
D2609 | 2 | 4 | 2
D504 | 2 | 2 | 2
D5850 |  | 2 | 
Q22 | 1 | 2 | 1
Q2610 | 2 | 2 | 2
Q2800 | 2 | 2 | 2
Q36 |  | 3 | 
Q41 | 2 | 2 | 2
Q48 | 2 | 2 | 2
Q57.1 |  | 1 | 
U1034 | 3 | 3 | 3
U1046 | 2 | 2 | 2
U1057 | 2 | 2 | 2
U1500 |  | 2 | 
U1512 | 2 | 2 | 2
U1517 | 2 | 2 | 2
U5403 | 2 | 2 | 2
U5852 | 3 | 3 | 3
U5853 | 3 | 3 | 3
U5950 | 2 | 2 | 2
Grand Total | 34 | 45 | 34

## Slide 6: Proposed logic – in progress
Machine calls and operator calls needs to be separated with the unique identifier
Remove overridden from the report
Remove machine data from the report
Only calculate the operator flagged data
  True call report
  False call report